L20 DOORS / SHUTTERS / HATCHES

610 ROLLER SHUTTERS

ALUMINIUM ROLLER SHUTTERS (AL50)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

SHOPPING MALLS, BARS, SERVING COUNTERS

Mainly used on openings where security is required without the cost of electrical operation.
A lightweight but strong Roller Shutter for shop windows, entrance doors, servery counters.
Also available punched to create a brick bond grille. Available in coloured polyester powder coating or mill finish aluminium.

- SIZE

Maximum Size recommended 2800mm x 2800mm.

- LEGISLATION COMPLIANT

Adhering to new legislation requiring all roller shutters to comply with the Construction Products Directive (C.P..D), all doors manufactured by BL Shutters are designed, manufactured and independently tested to meet the requirements of BS EN 13241 : 2003 & Construction Products Directive 89/106/EFC.

- FIXING

Vertical face or reveal fixed.

- BARREL

For openings up to 3 metres wide. Constructed from 100mm outside diameter steel tube with helicoil 
counter balance spring(s), mounted on 16mm steel shaft with nylon bearing blocks at each end.

- CURTAIN

Constructed from 50mm wide x 1.2mm interlocking galvanised aluminium laths.
Finished with aluminum ‘T’ section bottom rail with integral lift grip.

- SIDE GUIDES

Constructed from 3mm x 38mm aluminium guide channel bolted to 38mm x 38mm aluminium angle.

- OPERATION

Self coiling via helicoil counter balance springs.

- ELECTRICAL OPERATION

By means of 240 volt 500 watt (Maximum) tubular motor within tube.
Incorporating up/down limits and manual over-ride for emergency operation.

- OPTIONAL EXTRAS

Powder Coated Laths, Electrical Operation, Hoods, Bottom Draught Strip, 
Heavy Duty Weather Seal, Remote Control, Fascia.