L20 DOORS / SHUTTERS / HATCHES

610 ROLLER SHUTTERS

GARAGE ROLLER DOORS (BLG77)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

DOMESTIC GARAGES, CARPORTS

A foam filled double skin insulated garage door offering smooth running robust alternative to
other garage doors. Available with remote control via keyfob and manual override facility. 
A variety of different colours are available and oak and mahogany woodgrain finish to match
PVC windows. Small coil diameter offers clear height and width openings. The Roller Shutter 
is a proven design now available for domestic use. Available in colour polyester powder coated.

- SIZE

Maximum Size recommended 4500mm x 3500mm.

- LEGISLATION COMPLIANT

Adhering to new legislation requiring all roller shutters to comply with the Construction Products Directive (C.P.D), all doors manufactured by BL Shutters are designed, manufactured and independently tested to meet the requirements of BS EN 13241: 2003 & Construction Products Directive 89/106/EFC.

- FIXING

Vertical face or reveal fixed.

- BARREL

Constructed from hexagonal tube mounted on nylon bearing blocks incorporating motor drive.

- CURTAIN

Constructed from 77mm foam filled aluminium laths interlocking with riveted nylon end locks.
Standard colours.

- SIDE GUIDES

Constructed from extruded aluminium guide channel 90mm x 33mm polyester powder coated as
standard white or brown. Preformed in one piece guides include 2 neoprene strips for smooth shutter operation and also include weather brushes.

- ENDPLATES

300mm robust head plates with 45° bevel corner and reinforced profile edge. Fully enclosed with
coil casing.

Safety Brake fitted as standard.

- OPTIONAL EXTRAS

Remote Control, Photo electric safety cell.

- STANDARD COLOURS

White, brown, biege, green, red, black, wood grained teak.
Additional colours: Wood grained Oak and Wood grained Mahogany.