L20 DOORS / SHUTTERS / HATCHES

560 PVC STRIP CURTAINS

PVC SCREENS & DOORS (PVC)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

COLD STORES, WELDING BOOTHS, DOORWAYS

Flexible PVC Strip Curtains or Crash Doors provide the most practical and economical 
solution to heat and noise pollution in the workplace. The most common benefits are
reducing heat loss, workplace safety helping to exclude birds and vermin.
Also available in polar grade for low temperatures and cold rooms. Available in clear PVC or various colours.

- SIZE

Maximum Size recommended 8000mm X 8000mm

- FIXING

Vertical face or fixed under lintel.

- PVC CRASH DOORS FRAME

The framework is manufactured from 43mm O/D (32mm I/D) heavy wall steam tube with a 5mm 
horizontal triangular shaped mild steel gusset plate of varying size (according to width of door). 
A separate clamping strip is used to clamp the flexible pandelin position, and is held in place with special mild steel rivets and collars. An adjustable bearing is fitted to the bottom of the vertical tube to locate onto a hardened steel cone secured to the floor.

- PVC CRASH DOORS SPRING UNIT

The double action spring unit is concealed within the top of the vertical tube. The coil is of a high 
quality spring steel, and is held between the best malleable iron bearings on a 19mm diameter mild 
steel spindle. The spindle is welded to a mild steel plate 200mm x 51mm x 6mm for 
fixing to the lintel. The tension of the coil can be adjusted to suit on site conditions, without being 
overstressed. One unit is fitted to each floor leaf. Constructed from 75mm wide curved interlocking 
galvanised steel lath with mild steel endlocks and galvanised steel bottom rail.

- PVC STRIP CURTAINS INFO

A glass-clear, ultra-violet stabilised and abrasive resistant PVC material, extruded with round edges 
to reduce the possibility of injury to pedestrians. The material is flexible, tear resistant and flame 
retardent,(complies with BS 476 part 7).
• Artic quality for cold stores and chilled room applications.
• Orange standard quality width markers for aperture definition.
• Buffer quality for extra resistance to the constant buffeting by heavy loads or forklift trucks.
• Transparent Green allows through access and vision but safety inhibits welding flash.