L20 DOORS / SHUTTERS / HATCHES

610 ROLLER SHUTTERS

COMMERCIAL ROLLER SHUTTER (SC75)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

Shops, Offices, Garages.

Retail and commercial environments benefit from the most commonly used roller shutters. Available in solid or perforated curved profile they can be manually self coiling or electrically operated for ease of use. Perforated roller shutters are an ideal solution for security when a high level of visibility is required. Available in coloured polyester powder coating, plastisol, or standard galvanised finish.

- SIZE

Maximum Size recommended 7500mm x 3500mm. (Larger on request)

- LEGISLATION COMPLIANT

Adhering to new legislation requiring all roller shutters to comply with the Construction Products Directive (C.P..D), all doors manufactured by BL Shutters are designed, manufactured and independently tested to meet the requirements of BS EN 13241 : 2003 & Construction Products Directive 89/106/EFC.

- FIXING

Vertical face or reveal fixed.

- BARREL

For openings up to 6 metres wide. Constructed from 100mm steel
tube mounted on 25mm steel bearings. Incorporating motor drive. 
For 6 metres and over 139mm tube.

- CURTAIN

Constructed from 75mm wide curved section, interlocking galvanised steel laths.
Finished with an aluminium section bottom rail.

- SIDE GUIDES

Constructed from 3mm x 65mm guide channel bolted to 75mm x 50mm steel angle.

- ELECTRICAL OPERATION

By means of tubular motor within tube. Incorporating up/down limits and manual
over-ride for emergency operation.

Safety Brake fitted as standard.

- ELECTRICITY SUPPLY

240 Volt 1 Phase

- OPTIONAL EXTRAS

Plastisol Coated Laths, Powder Coated Laths, Perforated Laths, Remote Control,
Hood, Weather Seals, Fascia.