L20 DOORS / SHUTTERS / HATCHES

610 ROLLER SHUTTERS

FIRE ROLLER SHUTTER (SFS75)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

SHOPPING MALLS, SCHOOLS, OFFICES, HOSPITALS

Offering fire protection in a wide range of colours to complement its surroundings, a fire
shutter is the most effective way of greatly reducing or containing the spread of fire.
Designed to provide a fire resistance rating of up to 240 minutes with respect to the 
integrity criteria of BS:476 Part 22 1987, as tested and assessed at B.R.E. Fire and Risk 
Sciences Division. Available in polyester powder coating or standard galvanised finish.

- SIZE

Maximum Size recommended 7000mm x 4000mm. (Larger on request)

- LEGISLATION COMPLIANT

As tested and certified by BRE London

Adhering to new legislation requiring all roller shutters to comply with the Construction Products Directive (C.P..D), all doors manufactured by BL Shutters are designed, manufactured and independently tested to meet the requirements of BS EN 13241 : 2003 & Construction Products Directive 89/106/EFC.

- FIXING

Vertical face or reveal fixed.

- BARREL

Constructed from mild steel tube with helicoil counter balance springs mounted on mild steel shaft,
with mild steel bearing blocks at each end.
Incorporating high speed bearings. Tube and shaft size vary according to opening size.

- CURTAIN

Constructed from 75mm wide curved interlocking galvanised steel lath
with mild steel endlocks and galvanised steel bottom rail.

- SIDE GUIDES

Constructed from 3mm x 63mm channel incorporating drop bar guides.
Bolted to 75mm x 50mm mild steel angle.

- OPERATION

Electric motor connected to solenoide or fusible link release mechanism.

Safety brake fitted as standard.

- ELECTRICAL SUPPLY

240 Volt, 1 Phase
415 Volt, 3 Phase

- OPTIONAL EXTRAS

Solenoide release mechanism.
Fusible link release mechanism.

Fire Interface.