L20 DOORS / SHUTTERS / HATCHES

610 ROLLER SHUTTERS

INDUSTRIAL ROLLER SHUTTER (SI75)

- MANUFACTURER

BL Shutters Ltd, Carn Rd, Carn Industrial Estate, Portadown, Co Armagh.

Telephone: 028 38333551. Fax: 028 38350204.

Email: sales@blshutters.co.uk . Website: www.blshutters.co.uk

- APPLICATION

Warehousing, factories, Farm buildings.

One of the most commonly used roller shutters offering a clear height and width access through external openings. This is a proven design used for decades on a diverse range of openings on industrial and retail applications giving a durable and economic solution. Available in coloured polyester powder coating, plastisol, or standard galvanised finish.

- SIZE

Maximum Size recommended 6000mm x 6000mm. (Larger on request)

- LEGISLATION COMPLIANT

Adhering to new legislation requiring all roller shutters to comply with the Construction Products Directive (C.P.D), all doors manufactured by BL Shutters are designed, manufactured and independently tested to meet the requirements of BS EN 13241 : 2003 & Construction Products Directive 89/106/EFC.

- FIXING

Vertical face or reveal fixed.

- BARREL

For openings up to 6 metres wide. Constructed from 139mm outside diameter x 126mm
inside diameter steel tube, mounted on 25mm steel shaft, with steel bearings at each end. 
Incorporating high speed bearings. Finish one coat of Red Oxide paint.

- CURTAIN

Constructed from 75mm wide curved section, interlocking galvanised steel laths. Finished with a 
galvanised ‘T’ section bottom rail.

- SIDE GUIDES

Constructed from 3mm x 63mm guide channel bolted to 75mm x 50mm steel angle.

Openings 4500 x 4500 and above will be fitted with windlock guides.

- GEARING

By means of continuous galvanised hand chain, driving mild steel sprockets connected by high speed roll chain.

- ELECTRICAL OPERATION

By means of 1/2 HP up to 2HP geared motor complete with rotary limits and emergency hand chain 
mechanism. 3 push button controls as standard.

Safety brake fitted as standard.

- ELECTRICITY SUPPLY

240 Volt 1 Phase, 415 Volt 3 Phase.

- OPTIONAL EXTRAS

Plastisol Coated Laths, Powder Coated Laths, Wicket Gate, Hood, Bottom Draught Strip,
Heavy Duty Weather Seal, Remote Control, Fascia.